Chapter 5 Transmission Lines

5-1 Characteristics of Transmission Lines

Transmission line: It has two conductors carrying current to support an EM wave, which is TEM or quasi-TEM mode. For the TEM mode, , , and .

The current and the EM wave have different characteristics. An EM wave propagates into different dielectric media, the partial reflection and the partial transmission will occur. And it obeys the following rules.

Snell’s law:  and θi=θr

The reflection coefficient: Γ= and the transmission coefficient: τ=

for perpendicular polarization (TE)

for parallel polarization (TM)

In case of normal incidence, , where η1=and η2=.

Equivalent-circuit model of transmission line section:

, , ,

Transmission line equations: In higher-frequency range, the transmission line model is utilized to analyze EM power flow.

Set v(z,t)=Re[V(z)ejωt], i(z,t)=Re[I(z)ejωt]

where γ=α+jβ=

Characteristic impedance: Z0=

Note:

- International Standard Impedance of a Transmission Line is Z0=50Ω.

- In transmission-line equivalent-circuit model, G≠1/R.

Eg. The following characteristics have been measured on a lossy transmission line at 100 MHz: Z0=50Ω, α=0.01dB/m=1.15×10-3Np/m, β=0.8π(rad/m). Determine R, L, G, and C for the line.

(Sol.) , 1.15×10-3+j0.8π=

, ,

,

Eg. A d-c generator of voltage and internal resistance is connected to a lossy transmission line characterized by a resistance per unit length R and a conductance per unit length G. (a) Write the governing voltage and current transmission-line equations. (b) Find the general solutions for V(z) and I(z).

(Sol.) (a)

(b)

Lossless line (R=G=0):

Low-loss line (R<<ωL, G<<ωC):

Distortionless line (R/L=G/C):

Large-loss line (ωL<<R, ωC<< G):

,

Eg. A generator with an open-circuit voltage vg(t)=10sin(8000πt) and internal impedance Zg=40+j30(Ω) is connected to a 50Ω distortionless line. The line has a resistance of 0.5Ω/m, and its lossy dielectric medium has a loss tangent of 0.18%. The line is 50m long and is terminated in a matched load. Find the instantaneous expressions for the voltage and current at an arbitrary location on the line.

(Sol.) 0.18%=, Vg=10j

∵ Distortionless, ∴ , =0.01Np/m,

, γ=α+jβ=0.01+j5.58

, ,

Relationship between transmission-line parameters:

G/C=σ/ε and LC=με

Two-wire line: ,

Coaxial-cable line: , ,

Eg. It is desired to construct uniform transmission lines using polyethylene (εr=2.25) as the dielectric medium. Assume negligible losses. (a) Find the distance of separation for a 300Ω two-wire line, where the radius of the conducting wires is 0.6mm; and (b) find the inner radius of the outer conductor for a 75Ω coaxial line, where the radius of the center conductor is 0.6mm.

(Sol.) Two-wire line: , , a=0.6mm, ε=2.25ε0

Coaxial line: ,

a=0.6mm, b=3.91mm

Parallel–plate transmission line:

,

At y=0 and y=d, Ex=Ey=0, Hy=0

At y=0, ,

At y=d, ,

,

,

Lossy parallel–plate transmission line:

Surface impedance:

Eg. Consider a transmission line made of two parallel brass strips σc=1.6×107S/m of width 20mm and separated by a lossy dielectric slab μ=μ0, εr=3, σ=10-3S/m of thickness 2.5mm. The operating frequency is 500MHz. (a) Calculate the R, L, G, and C per unit length. (b) Find γ and Z0.

(Sol.) (a) ,

,

(b) γ==18.13∠-0.41°, ω=2π×500×106, Z0==27.21∠0.3°

Eg. Consider lossless stripline design for a given characteristic impedance. (a) How should the dielectric thickness d be changed for a given plate width w if the dielectric constant εr is doubled? (b) How should w be changed for a given d if εr is doubled? (c) How should w be changed for a given εr if d is doubled?

(Sol.)

(a) ,  (b)

(c)

Attenuation constant of transmission line: α=, where PL(z) is the time-average power loss in an infinitesimal distance.

Suppose no reflection, ,

Microstrip lines: are usually used in the mm wave range.

, ,

Assuming the quasi-TEM mode:

Case 1: t/h＜0.005, t is negligible.

Given h, W, and εr, obtain Z0 as follows:

For W/h1: ,

where

For W/h1: ,

where

Given Z0, h, and εr, obtain W as follows:

For W/h2: , where

For W/h>2: , where

Case 2: t/h＞0.005. In this case, we obtain Weff firstly.

For W/h:

For W/h:

And then we substitute Weff into W in the expressions in Case 1.

Assuming not the quasi-TEM mode:

, where ,  (h in cm)

and , G=0.6+0.009Z0,  (f in GHz)

The frequency below which dispersion may be neglected is given by , where h must be expressed in cm.

Attenuation constant: α=αd +αc

For a dielectric with low losses:     ()

For a dielectric with high losses:     ()

For W/h → ∞: , where

For W/h:

For ＜W/h2: , where

and

For W/h2:

Eg. A high-frequency test circuit with microstrip lines.

5-2 Wave Characteristics of Finite Transmission Line

Eg. Show that the input impedance is Zi=.

(Proof)  ,

Let z=l, V(l)=VL, I(l)=IL

, Zi=

Lossless case (α=0, γ=jβ, Z0=R0, tanh(γl)=jtanβl): Zi=

Note: In the high-frequency circuit, the input current Ii=: the value in the low-frequency case. And the high-frequency Ii is dependent on the length l, the characteristic impedance Z0, the propagation constant γ of the transmission line, and the load impedance ZL. But the low-frequency Ii is only dependent on Z0 and ZL.

Eg. A 2m lossless air-spaced transmission line having a characteristic impedance 50Ω is terminated with an impedance 40+j30(Ω) at an operating frequency of 200MHz. Find the input impedance.

(Sol.) , , ,

Eg. A transmission line of characteristic impedance 50Ω is to be matched to a load ZL=40+j10(Ω) through a length l’ of another transmission line of characteristic impedance R0’. Find the required l’ and R0’ for matching.

(Sol.)

Eg. Prove that a maximum power is transferred from a voltage source with an internal impedance Zg to a load impedance ZL over a lossless transmission line when Zi=Zg*, where Zi is the impedance looking into the loaded line. What is the maximum power transfer efficiency?

(Proof) ,

When  and , , ∴

In this case, , ,

Transmission lines as circuit elements:

Consider a general case: Zi=

1. Open-circuit termination (ZL→∞): Zi=Zio=Z0coth(γl)

2. Short-circuit termination (ZL =0): Zi=Zis=Z0tanh(γl)

∴ Z0=, γ=

3. Quarter-wave section in a lossless case (l=λ/4, βl=π/2):

- Half-wave section in a lossless case (l=λ/2, βl=π):

Eg. The open-circuit and short-circuit impedances measured at the input terminals of an air-spaced transmission line 4m long are 250∠-50°Ω and 360∠20°Ω, respectively. (a) Determine Z0, α, and β of the line. (b) Determine R, L, G, and C.

(Sol.) (a) ,

(b) ,

,

Eg. Measurements on a 0.6m lossless coaxial cable at 100kHz show a capacitance of 54pF when the cable is open-circuited and an inductance of 0.30μH when it is short-circuited. Determine Z0 and the dielectric constant of its insulating medium.

(Sol.) (a) ,

Lossless=74.5Ω,

General expressions for V(z) and I(z) on the transmission lines:

Let Γ=, z’=l-z

For a lossless line, V(z)=

Eg. A 100MHz generator with Vg=10∠0° (V) and internal resistance 50Ω is connected to a lossless 50Ω air line that is 3.6m long and terminated in a 25+j25(Ω) load. Find (a) V(z) at a location z from the generator, (b) Vi at the input terminals and VL at the load, (c) the voltage standing-wave radio on the line, and (d) the average power delivered to the load.

(Sol.) , , , , ,

, ,

,

(a)

(b)

(c)

(d) ,

Eg. A sinusoidal voltage generator Vg=110sin(ωt) and internal impedance Zg=50Ω is connected to a quarter-wave lossless line having a characteristic impedance Z0=50Ω that is terminated in a purely reactive load ZL=j50Ω. (a) Obtain the voltage and current phasor expressions V(z’) and I(z’). (b) Write the instantaneous voltage and current expressions V(z’,t) and I(z’,t).

(Sol.) (a)

(c) ,

,

(b)

Eg. A sinusoidal voltage generator with Vg=0.1∠0° (V) and internal impedance Zg=Z0 is connected to a lossless transmission line having a characteristic impedance Z0=50Ω. The line is l meters long and is terminated in a load resistance ZL=25Ω. Find (a) Vi, Ii, VL, and IL; (b) the standing-wave radio on the line; and (c) the average power delivered to the load.

(Sol.) (a) , ,

(b) , (c)

Eg. Consider a lossless transmission line of characteristic impedance R0. A time-harmonic voltage source of an amplitude Vg and an internal impedance Rg=R0 is connected to the input terminals of the line, which is terminated with a load impedance ZL=RL+jXL. Let Pinc be the average incident power associated with the wave traveling in the +z direction. (a) Find the expression for Pinc in terms of Vg and R0. (b) Find the expression for the average power PL delivered to the load in terms of Vg and the reflection coefficient Γ. (c) Express the ratio PL/Pinc in terms of the standing-wave ratio S.

(Sol.) , ,

(a)

(b)

(c)

Case 1 For a pure resistive load: ZL=RL

, 1. Γ=0S=1 when ZL= Z0 (matched load)

2. Γ=-1S=∞ when ZL=0 (short-circuit), 3. Γ=1S=-∞ when ZL=∞ (open-circuit)

occurs at

occurs at

If

If

If

Eg. The standing-wave radio S on a transmission line is an easily measurable quality. Show how the value of a terminating resistance on a lossless line of known characteristic impedance R0 can be determined by measuring S.

(Sol.) If , ,  occurs at  and  occurs at.

, , , ,  or .

If , ,  occurs at , and  occurs at .

, , , . or

Case 2 For a lossless transmission line, and arbitrary load:

ZL=, zm’+lm=λ/2

Find ZL=?

1. , 2. At θΓ=2βzm’-π, V(z’) is a minimum.

3. ZL=RL+jXL =

Eg. Consider a lossless transmission line. (a) Determine the line’s characteristic resistance so that it will have a minimum possible standing-wave ratio for a load impedance 40+j30(Ω). (b) Find this minimum standing-wave radio and the corresponding voltage reflection coefficient. (c) Find the location of the voltage minimum nearest to the load.

(Sol.)

, ,

,

Eg. SWR on a lossless 50Ω terminated line terminated in an unknown load impedance is 3. The distance between successive minimum is 20cm. And the first minimum is located at 5cm from the load. Determine Γ, ZL, lm, and Rm.

(Sol.)

=0.15m

,

Eg. A lossy transmission line with characteristic impedance Z0 is terminated in an arbitrary load impedance ZL. (a) Express the standing-wave radio S on the line in terms of Z0 and ZL. (b) Find the impedance looking toward the load at the location of a voltage maximum. (c) Find the impedance looking toward the load at a location of a voltage minimum.

(Sol.) (a)

(b)

(c)

5-3 Introduction to Smith Chart

,

: r-circle, : x-circle

Several salient properties of the r-circles:

- The centers of all r-circles lie on the Γr-axis.

- The r=0 circle, having a unity radius and centered at the origin, is the largest.

- The r-circles become progressively smaller as r increases from 0 toward ∞, ending at the (Γr=1, Γi=0) point for open-circuit.

- All r-circles pass through the (Γr=1, Γi=0) point.

Salient properties of the x-circles:

- The centers of all x-circles lie on the Γr=1 line, those for x>0 (inductive reactance) lie above the Γr–axis, and those for x<0 (capacitive reactance) lie below the Γr–axis.

- The x=0 circle becomes the Γr–axis.

- The x-circle becomes progressively smaller as |x| increases from 0 toward ∞, ending at the (Γr=1, Γi=0) point for open-circuit.

- All x-circles pass through the (Γr=1, Γi=0) point.

Summary

- All |Γ|–circles are centered at the origin, and their radii vary uniformly from 0 to 1.

- The angle, measured from the positive real axis, of the line drawn from the origin through the point representing zL equals θΓ.

- The value of the r-circle passing through the intersection of the |Γ|–circle and the positive-real axis equals the standing-wave radio S.

Application of Smith Chart in lossless transmission line:

,  when

keep |Γ| constant and subtract (rotate in the clockwise direction) an angle  from θΓ. This will locate the point for |Γ|ejφ, which determine Zi.

Increasing z’wavelength toward generator in the clockwise direction

A change of half a wavelength in the line length A change of  in φ.

Eg. Use the Smith chart to find the input impedance of a section of a 50Ω lossless transmission line that is 0.1 wavelength long and is terminated in a short-circuit.

(Sol.) Given , ,

- Enter the Smith chart at the intersection of r=0 and x=0 (point  on the extreme left of chart; see Fig.)

- Move along the perimeter of the chart  by 0.1 “wavelengths toward generator’’ in a clockwise direction to P1.

At P1, read r=0 and , or , .

Eg. A lossless transmission line of length 0.434λ and characteristic impedance 100Ω is terminated in an impedance 260+j180(Ω). Find (a) the voltage reflection coefficient, (b) the standing-wave radio, (c) the input impedance, and (d) the location of a voltage maximum on the line.

(Sol.) (a) Given l=0.434λ, R0=100Ω, ZL=260+j180

  - Enter the Smith chart at zL=ZL/R0=2.6+j1.8 (point P2 in Fig.)

  - With the center at the origin, draw a circle of radius . (=1)

  - Draw the straight line  and extend it to P2’ on the periphery. Read 0.22 on “wavelengths toward generator” scale. =, .

- The  circle intersects with the positive-real axis  at r=S=4.

- To find the input impedance:

1. Move P2’ at 0.220 by a total of 0.434 “wavelengths toward generator,” first to 0.500 and then further to 0.154 to P3’.

2. Join O and P3’ by a straight line which intersects the  circle at P3.

3. Read r=0.69 and x=1.2 at P3. .

- In going from P2 to P3, the  circle intersects the positive-real axis  at PM, where the voltage is a maximum. Thus a voltage maximum appears at (0.250-0.220) or 0.030 from the load.

Application of Smith Chart in lossy transmission line

∴ We can not simply move close the |Γ|-circle; auxiliary calculation is necessary for the e-2αz’ factor.

Eg. The input impedance of a short-circuited lossy transmission line of length 2m and characteristic impedance 75Ω (approximately real) is 45+j225(Ω). (a) Find α and β of the line. (b) Determine the input impedance if the short-circuit is replaced by a load impedance ZL= 67.5-j45(Ω).

(Sol.) (a) Enter  in the chart as P1 in Fig.

Draw a straight line from the origin O through P1 to P1’.

Measure ,

Record that the arc  is 0.20 “wavelengths toward generator”. , . .

(b) To find the input impedance for:

1. Enter on the Smith chart as P2.

2. Draw a straight line from O through P2 to P2’ where the “wavelengths toward generator” reading is 0.364.

3. Draw a –circle centered at O with radius .

4. Move P2’ along the perimeter by 0.2 “wavelengths toward generator” to P3’ at 0.364+0.20=0.564 or 0.064.

5. Joint P3’ and O by a straight line, intersecting the –circle at P3.

6. Mark on line  a point Pi such that .

7. At Pi, read .

5-4 Transmission-line Impedance Matching

Impedance matching by λ/4-transformer: R0’=

Eg. A signal generator is to feed equal power through a lossless air transmission line of characteristic impedance 50Ω to two separate resistive loads, 64Ω and 25Ω. Quarter-wave transformers are used to match the loads to the 50Ω line. (a) Determine the required characteristic impedances of the quarter-wave lines. (b) Find the standing-wave radios on the matching line sections.

(Sol.) (a) .

,

(b) Matching section No. 1:

,

Matching section No. 2:

,

Application of Smith Chart in obtaining admittance:

, , where

Eg. Find the input admittance of an open-circuited line of characteristic impedance 300Ω and length 0.04λ.

(Sol.) 1. For an open-circuited line we start from the point Poc on the extreme right of the impedance Smith chart, at 0.25 in Fig.

2. Move along the perimeter of the chart by 0.04 “wavelengths toward generator” to P3 (at 0.29).

3. Draw a straight line from P3 through O, intersecting at P3’ on the opposite side.

4. Read at P3’: , .

Application of Smith Chart in single-stub matching:

, where yB=R0YB, ys=R0Ys

∵ 1+jbs= yB, ∴ ys=-jbs and lB is required to cancel the imaginary part.

Using the Smith chart as an admittance chart, we proceed as yL follows for single-stub matching:

- Enter the point representing the normalized load admittance.

- Draw the |Γ|-circle for yL, which will intersect the g=1 circle at two points. At these points, yB1=1+jbB1 and yB2=1+jbB2. Both are possible solutions.

- Determine load-section lengths d1 and d2 from the angles between the point representing yL and the points representing yB1 and yB2.

Determine stub length lB1 and lB2 from the angles between the short-circuit point on the extreme right of the chart to the points representing –jbB1 and –jbB2, respectively.

Eg. Single-Stub Matching:

Eg. A 50Ω transmission line is connected to a load impedance ZL= 35-j47.5(Ω). Find the position and length of a short-circuited stub required to match the line.

(Sol.) Given , ,

1. Enter  on the Smith chart as . Draw a –circle centered at O with radius .

2. Draw a straight line from  through O to  on the perimeter, intersecting the –circle at , which represents . Note 0.109 at  on the “wavelengths toward generator” scale.

3. Two points of intersection of the –circle with the g=1 circle.

At : . At : ;

4. Solutions for the position of the stubs:

For  (from  to ):

For  (from  to ):

For  (from  to , which represents ):

For  (from  to , which represents ):

5-5 Introduction to S-parameters

S-parameters:  for analyzing the high-frequency circuits.

Define ,

,

, where , , , and .

New S-parameters obtained by shifting reference planes:

, , ,

, where

= and =

T-parameters: , where

and